## Slide 1: SHAF (Safe, Healthy, Active and Flexible)

## Slide 2: Team Information
Students:
Ahmed Abdulkareem - Undergraduate Computer Engineer
Hai Dang Hoang - Undergraduate Computer Engineer
Todd Harlow - Undergraduate Computer Engineer
Thanh Tien Truong - Undergraduate Computer Engineer
Supervisor:
Mark Faust - Assistant Professor

## Slide 3: Topics
What is the challenge we want to focus on?
What is our solution to that challenge ?
How can we implement our solution ?
What work have we done so far ?
What are our next steps ?

## Slide 4: Challenge and Solution
45 million American adults have gym memberships in recent year
Many people don’t maximize the benefits of the exercises they perform because they don’t train the muscle intensely enough.
35 percent increase in workout-related injuries in recent years due to improper technique or inappropriate exercises
The ideal solution:
Inexpensive and easy-to-use device
Effective at providing correct methods for many exercises
Accurate at alerting users to when they should stop

## Slide 5: Objective
To design and prototype a wearable device that can effectively support a user’s workout by allowing them to select their targeted muscle group and a corresponding exercise. Our device will provide users examples of the chosen exercise, count correct repetitions, and accurately alert them when they should stop the exercise. The device should be safe, easy to use, and portable.

## Slide 6: Current Existing Solutions and Our Solution
A device that can:
  Measure the intensity of muscle activity
  Record the results
  Correct your form
  Detect muscle fatigue
  Be used by anyone who wishes to improve their workouts and avoid injury
 | Personal Trainers
Cost | 1
Effectiveness | 5
Flexibility | 4
Ease of use | 5
Support all types of exercise | 5
Total | 20
Workout Videos
3
3
2
5
5
18
Videos Recording
5
3
2
4
3
17
Our Solution
4
4
5
5
3
21

## Slide 7: Main Use Cases
Are my biceps “pumped”?
How many correct reps have I done so far?
When should I stop?
How can I perform an exercise correctly?
Measure the intensity of a given muscle’s activity
Count the number of reps
Detect the muscle fatigue index
Provide video examples

## Slide 8: Our Technical Solution
We use surface electromyography (sEMG) sensors to capture the voltage difference created by a contracting muscle
We employ both simple and complex digital signal processing to extract key features
sEMG signals
Is the muscle active ?
When is the muscle contracted / relaxed ?
How intense is the muscle activity?
Is the muscle fatigued?
Time-domain processing
Frequency-domain processing

## Slide 9: Our Physical Solution
A wearable sleeve working in conjunction with an Intel powered smart device
A wearable sleeve will measure sEMG signals and transmit data to a smart device
The smart device will let users choose the target muscle, the specific exercise for that muscle, and provide feedback

## Slide 10: Our Solution Summary
sEMG sensors to record muscle data
  Wearable garment containing custom-made sEMG electrodes and supporting circuitry.
  Communicates via Bluetooth to smart device
Intel Atom powered smart device to process data
  Time-domain processing for muscle activation
  Frequency-domain processing for muscle fatigue
Device will also provide user interface
  Audio and visual cues to keep user informed

## Slide 11: Flowchart for Our Solution
Wearable sleeve with sEMG sensors
Time-domain analysis
Frequency-domain analysis
Intel Atom
Is the muscle active?
When is the muscle contracted/relaxed?
How intense is the muscle activity?
Is the muscle fatigued?
User Interface

## Slide 12: Risks
What if the Intel Atom cannot handle all the signal and user interface processing?
What if our custom-made electrodes fail to provide an adequate signal?
Shift some or all signal processing
to an FPGA
We will use the off the shelf electrodes

## Slide 13: Our Current Achievements
Successfully detected when muscle is contracted or relaxed and can count repetitions
Making progress on detecting muscle fatigue
Completed a concept for user interface
Muscle Sensor V3 (sEMG sensor)

## Slide 14: Muscle is contracted/relaxed
bicep
tricep
Doing multiple curls (sEMG signal for bicep and tricep)

## Slide 15: Muscle is contracted/relaxed
sEMG signal from the sensor
ADC
Within acceptable range of upper bound threshold?
Within acceptable range of lower bound threshold?
Not in range
in range (contracted)
Increment rep
in range (relaxed)
ADC
Not in range

## Slide 16: Demo Video
https://www.youtube.com/watch?v=X1IopbZivjs&fea

## Slide 17: Detecting Muscle Fatigue
Key idea:
Mean or median frequency will decrease when muscle is fatigued
Konrad, P. (2006). The ABC of EMG – A Practical Introduction to Kinesiological Electromyography. Noraxon U.S.A. Inc

## Slide 18: Detecting Muscle Fatigue
Bicep signal, normal curls
Bicep signal, fatigued curls

## Slide 19: Detecting Muscle Fatigue
sEMG signal from the sensor
Apply FFT
Compute mean or median power frequency
Our mean and median power frequency increases
Different from our expectation
Do the comparison

## Slide 20: User Interface
Select target muscle
Select exercise
Watch the example video
Perform the exercise and observe the results
Bicep
Tricep
Each exercise will have it own video
Human body graphic shows which muscle is active
Alert user when the target muscle is fatigued
Dumbbell Bicep Curl
Barbell Curl
Drag Curl
Body-Up
Cobra Triceps Extension

## Slide 21: Where are we currently at ?
Obtain information and ideas
Define requirements and create specifications
Get needed equipment
Get samples and do signal analysis
Create GUI and work on Bluetooth communication
Test the device
Deliver
Create a wearable garment

## Slide 22: How much we have spent so far ?
Equipment | Cost per unit | Quantity | Total
Muscle Sensor V3 | $50 | 3 | $150
Arduino Uno Board | $20 | 2 | $40
Electrical Components kit | $40 | 1 | $40
Wearable Garment | $82 | 1 | $82
Total | $312 |  | 

## Slide 23: Next Steps
Create a GUI for the device
Learn Bluetooth communication using the Intel Atom
Develop an effective method to detect muscle fatigue index accurately
Create a wearable garment
Test the prototype
New resource required:
Intel Atom
Combine all the parts to create the prototype

## Slide 24: Schedule and Additional Cost
Task | Time
Create GUI | Mid February - April
Learn Bluetooth communication | 1 month after we receive the Atom board
Develop method to detect muscle fatigue | Mid February - March
Create wearable garment | Mid February - March
Create working prototype | March – Mid April
Testing | Mid April - May
Additional Equipment | Cost per Unit | Quantity | Total
Electrodes | $6 | 10 | $60
Total | $60 |  | 

## Slide 25: Summary
Device Information
Purpose:
Improve individual workout quality
Functionality:
Use sEMG signal
  to measure muscle activity
  to detect muscle fatigue
Provide user interface
  to provide workout videos
  to record workout results
Time expectation
Budget
Device is ready for testing:
Mid April
Device is ready for delivery:
Early May
Have been used:
$312
Additional Cost:
$60

## Slide 26: Thank you for listening