## Slide 1: Filtering & Sample Rate
Typical sEMG signal: < 10 mV
Typical gain needed: 100 to 5000
  Signal amp as close as possible to electrode(s)
Typical high-pass filter: 5 to 60 Hz
Typical low-pass filter: 500 Hz
  1000 Hz sample rate (Nyquist rule)

## Slide 2: Preprocessing for Classification
Classwise Principal Component Analysis(cPCA)
  Data rotated by class-specific rotation matrices to specially de-correlate before feature extraction
  “Tunes” the data for better classification
Independent Component Analysis (ICA)
  Estimates set of independent signals from a mixture of signals using an un-mixing matrix
  Reduces crosstalk

## Slide 3: Decoding Myoelectric Information
Pattern based
  Calculates feature vectors from signal segments
  Inputs vectors into a classifier for prediction
Non-pattern based
  Proportional, onset analysis, finite state machines
  No 1-to-1 mapping, simple, no “training”

## Slide 4
Fig. 2. Schematic diagrams of pattern and non-pattern recognition-based sEMG control methods.
Maria Hakonen, Harri Piitulainen, Arto Visala
Current state of digital signal processing in myoelectric interfaces and related applications
Biomedical Signal Processing and Control, Volume 18, 2015, 334–359
http://dx.doi.org/10.1016/j.bspc.2015.02.009

## Slide 5: Windowing
sEMG needs to be analyzed in real-time
Analysis is performed on windows of time
Two important system parameters:
  Classification accuracy
  System response time
Controlling parameters:
  Windowing technique
  Window length
  EMG signal state

## Slide 6: Windowing Technique
Overlapped windowing is better than adjacent
  Better classification accuracy
  Steadier controller delay
  Reduced maximum delay

## Slide 7: Window Length
Longer windows improve classification accuracy but decrease response time
Shorter windows increase errors
  Not “controllable” at error percentages >35%
Ideal window length: 50 to 400 ms
  50 to 400 samples @ 1000 Hz
  25 to 200 samples @ 500 Hz

## Slide 8: EMG Signal State
Transient state
  An abrupt change in contraction level or position
Steady state
  Muscle is under constant contraction
  More accurate signal classification
  Accuracy decreases less relative to window length