## Slide 1: Wearable Muscle Sensing Exercise System
Senior Capstone Project
Electrical & Computer Engineering
Maseeh College of Engineering & Computer Science:
Portland State University

## Slide 2: Team Information
Students:
Ahmed Abdulkareem - Undergraduate Computer Engineer
Hai Dang Hoang - Undergraduate Computer Engineer
Todd Harlow - Undergraduate Computer Engineer
Thanh Tien Truong - Undergraduate Computer Engineer
Supervisor:
Mark Faust - Assistant Professor

## Slide 3: Topics
What is the challenge we want to focus on?
What is our solution to that challenge ?
How can we implement our solution ?
What work have we done so far ?
What are our next steps ?

## Slide 4: Challenge and Solution
45 million American adults have gym memberships in recent year
Many people don’t maximize the benefits of the exercises they perform because they don’t train the muscle intensely enough.
35 percent increase in workout-related injuries in recent years due to improper technique or inappropriate exercises
The ideal solution:
Inexpensive and easy-to-use device
Effective at providing correct methods for many exercises
Accurate at alerting users to when they should stop

## Slide 5: Objective
To design and prototype a wearable device that can effectively support a user’s workout by allowing them to select their targeted muscle group and a corresponding exercise. Our device will provide users examples of the chosen exercise, count correct repetitions, and accurately alert them when they should stop the exercise. The device should be safe, easy to use, and portable.

## Slide 6: Current Existing Solutions and Our Solution
A device that can:
  Measure the intensity of muscle activity
  Record the results
  Correct your form
  Detect muscle fatigue
  Be used by anyone who wishes to improve their workouts and avoid injury
 | Personal Trainers
Cost | 1
Effectiveness | 5
Flexibility | 4
Ease of use | 5
Support all types of exercise | 5
Total | 20
Workout Videos
3
3
2
5
5
18
Videos Recording
5
3
2
4
3
17
Our Solution
4
4
5
5
3
21

## Slide 7: Main Use Cases
How many correct reps have I done so far?
When should I stop?
What is my 1 RM value ?
Count the number of reps
Detect the muscle fatigue index
Provide calculation for 1RM

## Slide 8: Our Technical Solution
We use surface electromyography (sEMG) sensors to capture the voltage difference created by a contracting muscle
The signal will be amplified, rectified and integrated before being sent to the microprocessor
sEMG signals
Do the user perform a correct rep ?
Have the user’s muscle been fatigue yet ?
Baseline and threshold comparison

## Slide 9: Design
Wearable sleeve with sEMG sensors
Get data samples and analyze the data
Arduino board
Let users select muscle types
Let users select exercise types
Let user see their workout results
iPhone apps
Amplify, rectify and integrate the captured signal
Capture the signal generated by the targeted muscle

## Slide 10
Design (Arduino)
Calibration
Correct reps and fatigue detector
1 KHz
ADC converter
Timeout
Processed Signal
Threshold
Calibration’s flags
Detector’s flag
Timeout’s flag
Timer

## Slide 11
Design (Arduino - Timer)
1 KHz
Initialization:
Timeout_Count = 0
Timeout = 0

## Slide 12
Design (Arduino - Calibration)
(I): Send from iPhone to Arduino
(A): Send from Arduino to iPhone

## Slide 13
Design (Arduino – Correct reps and fatigue detector)
(I): Send from iPhone to Arduino
(A): Send from Arduino to iPhone

## Slide 14: Data Collection Testing our setup with many subjects
Methodology
  24 subjects total (13 male, 11 female)
  Using resistance bands, each subject performed 4 sets of bicep curls until they felt they couldn’t do another
  Reps were counted and recorded
  Fatigue assumed to be at or near last rep
Testing our equipment
  Electrode Sleeve->Muscle Sensor->Arduino
  Log file from Arduino terminal used capture data
  Muscle Sensor output also sent to oscilloscope
  Plotted Arduino data compared to scope for verification
Observations
  Wide variety in how people perform bicep curls
  Some subject’s arms too small for proper sleeve fit
  Inconsistency in self-reported fatigue
    (Some users worked until failure and others did not)
“Am I doing this right?”
“Try keeping your back straight.”
“I like to lunge when I curl!”

## Slide 15: MATLAB Analysis Testing and tuning our algorithms using the data we collected
Repetition Detection
  Parameters = { BASELINE, THRESHOLD }
  Initial parameters used to detected first rep
  First rep used to calibrate parameters
    (1st Rep Peak ) * {BASELINE, THRESHOLD}
  Subsequent reps detected using new parameters
Fatigue Detection
  Parameter = { FATIGUE }
  Percent difference between last two reps compared to parameter
  Remains constant during processing
This is not a real plot of our data

## Slide 16: MATLAB Analysis Testing and tuning our algorithms using the data we collected
Batch Processing – Rep Detection
  100 runs for each data set
  10 BASELINE fractions, 10 THRESHOLD fractions
  10x10 output matrix of rep counts
  Absolute difference between observed count for data set and each matrix element
  All difference matrices summed
  Index of summed matrix that’s closest to zero represents the ideal BASELINE and THRESHOLD fraction
Bad Rep Detection:
“calibration” failed, only 4 reps recorded out of many
Good Rep Detection:
“calibration” succeeded, all reps counted correctly
Time (s)
Time (s)
Amplitude (ADC bits)
Amplitude (ADC bits)
NOTE: Red squares denote when the algorithm detects a new rep
Ideal BASELINE = 0.35
Ideal THRESHOLD = 0.60

## Slide 17: MATLAB Analysis Testing and tuning our algorithms using the data we collected
Batch Processing – Fatigue Detection
  This method assumes that fatigue should first be detected on or near the last rep
  16 runs for each data set
  16 different “fatigue threshold” fractions
  16x4 output matrix
    1st Column: Fatigue Threshold used for processing
    2nd Column: Observed Rep Count
    3rd Column: Rep # where fatigue first observed
    4th Column: Difference between 1 & 2
  All result matrices summed
  Index of summed matrix where column 4 is closest to zero represents the ideal “fatigue threshold” fraction
Ideal FATIGUE THRESHOLD = 0.16

## Slide 18: Electrode Sleeve Measures muscle activity via electrical signals on the user’s skin
Electromyography
  Activated motor units in muscles produce voltage differentials
  Amplitude: < 10 mV
  Frequency Range: 20 – 500 Hz
Electrode Styles
  Needles inserted into the muscle (OUCH!)
  Contacts placed onto skin surface (MUCH BETTER )
Implementation
  Followed example from Muscle Sensor website
  Uses conductive fabric as surface electrodes
  Uses button snaps to easily connect leads to Muscle Sensor
  Wetting electrodes before use greatly reduces signal noise and fluctuations
Example sleeve from Muscle Sensor website
The three sleeves made for our project

## Slide 19: Muscle Sensor V3 Conditions the electrode’s signal to work with the analog-to-digital converter on the Arduino
Amplify
  Input signal from electrodes is weak ( ~10 mv )
  Boosts signal up to + supply voltage ( 5 V )
Rectify
  Transforms +/- signal to + only
Smooth
  Integrates the rectified signal
Amplified
Rectified
Smoothed

## Slide 20: Arduino
Analog-to-Digital Converter
Converts analog signal from Muscle Sensor V3
Timer
Generates interrupts for 1kHz sample rate
SPI
Communicates with Bluetooth device
Main processor
Implements algorithm detect muscle fatigue
and rep count

## Slide 21: Bluetooth Device
Technical Specifications
  ARM Cortex M0 core running at 16 MHz
  256 KB flash memory
  32 KB SRAM
  Transport: SPI at 4MHz
Benefit using Bluetooth low energy (BLT)
  Short range
  Robust, efficient
  Low cost, low power
  Connectivity to mobile phones
  Stable
Bluefruit EZ-Link Shield V1.3

## Slide 22: SHAF Bluetooth Interaction view

## Slide 23: SHAF Bluetooth Communication Hierarchy

## Slide 24: Project Cost (Bill of Materials?)
Quantity | Item | Cost
1 | Arduino UNO | $25
1 | Muscle Sensor V3 | $25
1 | Electrode Sleeve | $15
 | TOTAL COST | $65

## Slide 25: Summary: What Worked
Electrode Sleeve
  When wetted properly, fabric electrodes reliably capture muscle activity
Time-domain rep detection
  Works well if user sleeve is worn properly and calibration is done correctly
Time-domain fatigue detection
  Works well in lab setting when consistently performing correct reps
Arduino/iPhone communication
  Devices work together using Bluetooth
iPhone app
  Successfully developed and deployed an iPhone app that controls our system

## Slide 26: Summary: What Didn’t Work
Frequency-domain fatigue detection failed
  We spent a lot of time trying to get this to work but it was a dead end
Data collected for MATLAB analysis was not ideal
  Exercises should have been better supervised
  User’s should have performed calibration reps similar to end product
  Definition of “fatigue” should have been clearer
  This affected the reliability of MATLAB analysis results
Time-domain fatigue detection did not work on collected data
  Partially due to analysis methodology (no concrete “fatigue rep” recorded)
  Literature not promising for time-domain fatigue detection in muscles
Project Schedule
  Never completed all revisions, ended up working week-to-week, creating ambiguity
Design Documentation
  A lack of documentation early in the project led to confusion about project goals and design decisions

## Slide 27: Summary: Lessons Learned
Research
  Rigorous research early in the project can prevent many missteps
Design, Design, Design!
  Every major component for a project should have a design document that is reviewed by the entire team
Collaboration
  Every team member should be familiar with the tools used for the project
  Project schedules help keep the project on track and maximize productivity
Specifications
  Key specs for project components should be clearly understood before ordering parts