## Slide 1: Analyzing Rec Center Data
15 subjects total (8 male, 7 female)
60 data sets from Arduino ADC (4 for each subject)
For all data sets:
  Median reps = 20 [5, 42]
  Median voltages generated = 63 [16, 327]
  Minimum voltages range = [0,20]
  Maximum voltages range = [81, 1023]

## Slide 2: Current State of Algorithm
Rep detection
  4 sets match observed count
  15 sets are +/- 2 reps
  Remainder are +/- >2 reps
  Range of differences: [-16, 109]
Fatigue detection
  Briefly worked for one data set
  Broke when I setup batch processing
  Currently no fatigue detected on any set

## Slide 3: Observations
The BASELINE value is currently fixed. This could be dynamically adjusted to make rep detection more robust
The THRESHOLD value is currently calculated from the first rep detected. This does not necessarily mimic how calibration will be in the final device.
The observed rep counts need to be hand verified due to data collection anomalies.